## Slide 1: On the performance characteristics of linear, multi-linear and non-linear tensor models for alarm prediction in multi-sensor data
Ahamed Buhari , Chandraprakash
Supervisiors : Hadi Fanaee, Mahmoud Rahat

## Slide 2
Introduction

## Slide 3
Examining different strategies for alarm prediction system for Alfa Laval’s Separator Machines
We investigate three types of tensor modelling:
  Linear
  Multi-linear
  Non-linear

## Slide 4: Objective
Alarm predictive model helps to overcome the problems of existing pre-defined thresholds alarm system.
The state of black box models versus white box tensor models

## Slide 5: Research Questions
Which strategy provides better/interpretable predictions?
Which sets of configuration settings makes a better predictive model.
  To determine the ideal window size for collecting samples prior to the occurrence of alarms and warnings.
  To determine what sampling frequency in time series is best for making better predictions.
  Best tuned models of different types together : fair comparison

## Slide 6: Novelty
Industrial novelty: unfortunately, currently no predictive model is being used in the company! This is the first effort towards using machine learning in alarm prediction
Scientific novelty: Providing guidance towards choosing the right modeling strategy with regards to the company’s data characteristics. No previous investigation is made on trade-off between black-box tensor models and white-box tensor models on real-world data.

## Slide 7
Methodology

## Slide 8
Fig: Flow Diagram of proposed method
Data Collection
Data Transformation
Dividing & Selecting window samples
Data Cleaning
Splitting Data
Predictive Model
The flow diagram is splited into three parts i.e., Data PreProcess, Data Transformation and Model Prediction. In data preprocess, raw data is cleaned and normalized then dividing and selecting the samples for further data transformation. After data transformation in Linear and Multi-Linear, model prediction is done in vector, matrix, tensor and non- linear models.
Methodology

## Slide 9
27 water purifier machines installed on different ships. These machines purifies oil and water supplies onboard marine vessels.
Alarm: 30.
Alarms types : A10, A13, A17, A33, A69, A501 , A502 and etc.
Sensors: 102
Features : PT201_16, PT201_71, LPS1_voltage_value, QIT201 and etc.
Time stamp
Sampling: 3-12 months, depending on the machine
Data Set

## Slide 10
The original data was in time series of irregular pattern of different sensors,
made it equally interval by resampling it.
The data is selected from 5 seconds before the point when the alarms or warning happens until one hour before of it.
Ignored the alarms of less data samples.
Data Preprocess

## Slide 11
Representation of generated Tensor Data after preprocessing
Time
Sensor

## Slide 12
W1
Y
720 Instants x 5 sec
ws = 30
Examples 30
150 Seconds
720x5-30x5 = 3450
TG= 5 Sec
W1
3450
Alarm
Dividing and Selecting window Samples
The total window is an one hour i.e. 720 time instants x 5 seconds of sampling frequncy which is 720x5 = 3600 seconds
Fig: Remaining useful life

## Slide 13
W2
3300
W End
0
W2
Y
720 Instants x 5 Sec
ws = 30
Examples 30
150 Seconds
720x5-300 = 3300
TG= 5 Sec
Alarm
W End
Y
720 Instants x 5 Sec
ws = 30
Examples 30
150 Seconds
720x5-3600 = 0
TG= 5 Sec
Alarm
Figuare (s1)
Figuare (s2)

## Slide 14
Data Transformation
Hankelization
Hankelization
Tensor
(Multi-linear)
Lag
Matrix
(Multi-linear)
Vector
(Linear)
In data transformation, It transformed in three forms Vector, Matrix and Tensor methods.
The concept of Hankelization is introduced in Tensor and Matrix. In Tensor method, includes an additional dimensionality known as lag.

## Slide 15
Model Prediction
Non Linear
Tensor
CNN
Tensor LSTM
Multi Linear
Matrix Regression
Tensor Regression
Linear
Linear Regression
Model prediction is done in linear regression (1-D Tensor), matrix regression (2D Tensor), tensor regression (3D Tensor) and non-linear models i.e., Tensor CNN (3d Tensor) and Tensor LSTM (3D Tensor) models and examine the performance with different experimental configuration.

## Slide 16: Experimental Configuration
Machines used : 13, 14 & 15
Alarm Types : A33, A69, A502
Time Granularity : 5 sec, 7 sec, 10 sec, 13 sec, 15 sec, 20 sec.
Window Size : 1 min, 2 min, 3 min, 5 min, 10 min, 15 min, 20 min.
Lag Size : 1, 2, 3, 4, 5, 6, 7, 8, 10.

## Slide 17
Convolutional Neural Network
The convolutional neural networks is the ability to automatically learn a large number of filters in parallel specific to a training dataset under the constraints of a specific predictive modelling.
In our experiment results, the below architecture convolutional model performed the best with the following parameter.

## Slide 18
Long Short-Term Memory
LSTM is known and capable for learning order dependency in sequence prediction problems. We have used Multivariate LSTM model. In our experiment result, the below architecture LSTM model performed the best with the following parameter.

## Slide 19: Results

## Slide 20
Alarm A33 | Machine 13 |  | Machine 14 | 
Methods | Configuration | Train MAE | Configuration | Train MAE
Tensor Regression | (TG:5,W:10,L:2,S1806) | 624.4 | (TG:20,W:5,L:8,S543) | 688.2
Tensor-Convolutional Neural Network | (TG:20,W:5,L:8,S903) | 816.9 | (TG:20,W:5,L:8,S903) | 867
Vector linear Regression | (TG:5,W:5,S3612) | 980.3 | (TG:5,W:5,S2172) | 926.5
Matrix Regression | (TG:5,W:10,S1806) | 721.4 | (TG:5,W:10,S1086) | 776.8
Tensor - lstm | (TG:10,W:1,L4,S9030) | 894.2 | (TG:15,W:10,L6,S362) | 903.1
Alarm A33 | Machine 13 |  | Machine 14 | 
Methods | Configuration | Test MAE | Configuration | Test MAE
Tensor Regression | (TG:5,W:10,L:2,S1806) | 883.6 | (TG:20,W:5,L:8,S543) | 923.6
Tensor-Convolutional Neural Network | (TG:20,W:5,L:8,S903) | 843.2 | (TG:20,W:5,L:8,S903) | 835.3
Vector linear Regression | (TG:5,W:5,S3612) | 1104.8 | (TG:5,W:5,S2172) | 1193.8
Matrix Regression | (TG:5,W:10,S1806) | 1034.1 | (TG:5,W:10,S1086) | 1080
Tensor - lstm | (TG:10,W:1,L4,S9030) | 920.4 | (TG:15,W:10,L6,S362) | 965.7
Alarm A33 is present in Machine 13, 14 and 15. The train mean absolute error of tensor regression is optimal in all the machines with different configuration settings such as TG (Time granularity), window size and lag values.
Tensor convolutional neural network is robust to overfitting , as we can see there is a low variance in the train and test cases.
Train Results for Alarm A33
Test Results for Alarm A33

## Slide 21
Train Results for Alarm A33
Test Results for Alarm A33
Alarm A33 | Machine 15 | 
Methods | Configuration | Test MAE
Tensor Regression | (TG:20,W:5,L:8,S897) | 1058.1
Tensor-Convolutional Neural Network | (TG:15,W:10,L:8,S598) | 775.6
Vector linear Regression | (TG:5,W:1,S17940) | 1208
Matrix Regression | (TG:15,W:10,S598) | 1124.3
Tensor - lstm | (TG:15,W:2,L6,S1810) | 954.3
Out of these three machines, Alarm A33 has a better performance in machine 15 with configuration settings (TG:20,W:5.L:8,S:897).However the variance is high in
Tensor regression for all machines due to the non-linearity of the data.
Alarm A33 | Machine 15 | 
Methods | Configuration | Train MAE
Tensor Regression | (TG:20,W:5,L:8,S897) | 611.5
Tensor-Convolutional Neural Network | (TG:15,W:10,L:8,S598) | 662.3
Vector linear Regression | (TG:5,W:1,S17940) | 883.9
Matrix Regression | (TG:15,W:10,S598) | 664.3
Tensor - lstm | (TG:15,W:2,L6,S1810) | 949.8

## Slide 22
Alarm A502 is present in Machine 13 and 15. It is observed that Tensor regression outperforms other methods, and has a better performance in machine 15 with a configuration settings (TG:5, W:2, L:2, S 360)
Train Results for Alarm A502
Alarm A502 | Machine 13 |  | Machine 15 | 
Methods | Configuration | Train MAE | Configuration | Train MAE
Tensor Regression | (TG:5,W:2,L:2,S330) | 580.8 | (TG:5,W:2,L:2,S360) | 480.4
Tensor-Convolutional Neural Network | (TG:10,W:1,L:2,S660) | 824.2 | (TG:5,W:1,L:2,S720) | 827.2
Vector linear Regression | (TG:5,W:3,S220) | 974.9 | (TG:5,W:2,S360) | 774.6
Matrix Regression | (TG:5,W:2,S330) | 584.5 | (TG:15,W:1,S240) | 589.1
Tensor - lstm | (TG:10,W:1,L4,S330) | 834.8 | (TG:5,W:1,L2,S720) | 969.4
Test Results for Alarm A502
Alarm A502 | Machine 13 |  | Machine 15 | 
Methods | Configuration | Test MAE | Configuration | Test MAE
Tensor Regression | (TG:5,W:2,L:2,S330) | 1013.5 | (TG:5,W:2,L:2,S360) | 991.6
Tensor-Convolutional Neural Network | (TG:10,W:1,L:2,S660) | 935.3 | (TG:5,W:1,L:2,S720) | 980.9
Vector linear Regression | (TG:5,W:3,S220) | 1190.1 | (TG:5,W:2,S360) | 1150.1
Matrix Regression | (TG:5,W:2,S330) | 1137.2 | (TG:15,W:1,S240) | 1177.3
Tensor - lstm | (TG:10,W:1,L4,S330) | 972.8 | (TG:5,W:1,L2,S720) | 1252

## Slide 23
Train Results for Alarm A69
Alarm A69 | Machine 13 |  | Machine 14 | 
Methods | Configuration | Train MAE | Configuration | Train MAE
Tensor Regression | (TG:5,W:10,L:2,S1812) | 633.9 | (TG:20,W:5,L:8,S546) | 602.8
Tensor-Convolutional Neural Network | (TG:20,W:5,L:8,S906) | 808.9 | (TG:10,W:10,L:4,S546) | 794.6
Vector linear Regression | (TG:20,W:5,S906) | 880.3 | (TG:15,W:1,S3640) | 1057.6
Matrix Regression | (TG:15,W:5,S1208) | 864.4 | (TG:15,W:5,S1208) | 774.2
Tensor - lstm | (TG:15,W:2,L6,S330) | 834.8 | (TG:5,W:2,L2,S5460) | 885.4
Alarm A69 | Machine 13 |  | Machine 14 | 
Methods | Configuration | Test MAE | Configuration | Test MAE
Tensor Regression | (TG:5,W:10,L:2,S1812) | 1080.8 | (TG:20,W:5,L:8,S546) | 880.8
Tensor-Convolutional Neural Network | (TG:20,W:5,L:8,S906) | 831.1 | (TG:10,W:10,L:4,S546) | 829.1
Vector linear Regression | (TG:20,W:5,S906) | 1242.3 | (TG:15,W:1,S3640) | 1276.2
Matrix Regression | (TG:15,W:5,S1208) | 1124.6 | (TG:15,W:5,S1208) | 919
Tensor - lstm | (TG:15,W:2,L6,S330) | 972.8 | (TG:5,W:2,L2,S5460) | 923.4
Test Results for Alarm A69
Alarm A69 is present in Machine 13 and 14. The train performance in both the machines are almost similar, but the machine 14 has a clear edge over machine 13.
The settings of (TG:20,W:5,L:8,S:546) is the best optimal settings for Alarm A69.

## Slide 24
Conclusion & Plan ahead

## Slide 25
Conclusion
The proposed Tensor representation method performance on multi-sensor unequal-length time series machine dataset is better compared to Vector and Matrix models.
  Multi-linear methods outperforms linear method
Comparing multilinear and nonlinear method shows that multilinear modelling suffers from overfitting problem.
Tensor convolutional neural network is robust to overfitting however, train error is higher than Tensor Regression.
Tensor LSTM vs. Tensor CNN vs. Tensor Regression

## Slide 26
Plan Ahead
To reduce the variance of Tensor regression.
Final Report Preparation.
Final Presentation and submission.

## Slide 27
Thank you!!
&
Questions